## Slide 1: HydroStar Quick Start Guide

## Slide 2: HydroStar Main Menu
Load HydoStar by picking Hydro.bat installed in the C:\ directory
Decodes come from Carlson Software. Email support@carlsonsw.com for all HydroStar decodes.

## Slide 3: Download my emailed data files into the \HYDRO directory
The example job files are as following:
  1) Barge.veh (AutoCad drawing depicting barge for HydroStar.)
  2) exampe.pln (AutoCad drawing depicting site for HydroStar .)
  3) example.cl (A centerline going right to left in the site drawing starting with 0+00 stationing.)
You need to load these files in HydroStar
  1) Load Barge.veh in HydroStar’s main menu - pick OPTIONS then CONTINUE then OPTIONS then HYDROSTAR APPEARANCE then VEHICLE FILE then pick BARGE.VEH then BACK then BACK.
  2) To load both example.pln and example.cl in HydroStar’s main menu - pick PROJECT then LOAD PLAN VIEW FILE then pick EXAMPLE.PLN and then LOAD CENTERLINE FILE then pick EXAMPLE.CL then BACK.

## Slide 4: HydroStar Alignment
In HydroStar you need to setup the Datum and Zone your are working in. To set the Datum and Zone - pick OPTIONS then CONTINUE then OPTIONS then ALIGNMENT OPTIONS then ZONE then UTM (for this example) then UNIT then METRIC then BACK.
GPS Alignment needs to be entered and stored to a job file.
  Typically you have 2 to 4 control point.
  The 2 to 4 control points should be at the outside edges of the job.

## Slide 5: HydroStar Alignment
To align:
  From the HydroStar main menu - pick OPTIONS then CONTINUE then GPS SETUP. If the equipment does not display your receiver type, then pick EQUIPMENT and select your receiver then BACK.
  From HydroStar’s main menu - pick OPTIONS then CONTINUE then ALIGN then A for ADD.
    At this point one of 2 methods two create alignment RTK GPS points.
      1) If you have post processed the control points (Keep control points to only 2 to 4 points on the outside edges of your construction job.) Use Option 1 to type in UTM coordinates or your jobs control point coordinates. For RTK GPS points use Option 1 Enter Lat/Long/Z.
      2) If your control points are only known coordinate values not Lat/Long/Z values. Use Option 1 to type in UTM coordinates or your jobs control point coordinates. For RTK GPS points use Option 2 to Read GPS. This method you must travel and occupy the control points when reading GPS.
    When exiting Alignment store alignment file to a filename for recall.

## Slide 6: HydroStar Alignment (cont.)
The stored Alignment file needs to be Automatically loaded each time the rovers are started up. To do this in HydroStar’s main menu - pick OPTIONS then CONTINUE then OPTIONS then ALIGNMENT OPTIONS then pick AUTO LOAD LAST ALIGNMENT and change it to Yes then BACK then BACK.
Prior to Navigating make sure HydroStar is setup to read two RTK GPS receivers. From the HydroStar main menu - pick OPTIONS then CONTINUE then OPTIONS then GENERAL OPTIONS then check that both USE FIRST & SECOND GPS receiver is turned on and the proper COM ports.
Pick ROD HEIGHT and enter 12 then BACK then BACK to return to the main menu.

## Slide 7: Navigating the Barge with RTK GPS
The Alignment procedure permanently aligns the Base and Rover receivers to your jobs coordinates. Each day the Javad RTK GPS rover operator only needs to turn the units on and with all cables and power plugged in he goes to Monitor. When both Javad rovers are fixed he goes to Navigate and picks enter coordinates. The coordinates for each GPS receiver (#1 and #4) need to be calculated in advance for the exact location needed when pile driving. The operator enters those coordinates for point 1 (GPS Antenna #1) and point 2 (GPS Antenna #2). They will immediately go to a stakeout screen displaying the stakeout information for both receivers and will visually see the barge.veh in the plan view.
This screen needs to be viewed by the barge operator also. The barge operator navigates to point #1 so the first GPS Antenna is over the first stakeout coordinate values. Drop the pilon (anchor) and then pivot the barge to navigate so that the GPS Antenna #4 is over the second entered coordinate values. Drop pilons/Anchors!

## Slide 8: HydroStar additional menus
Plot Menu in HydroStar allow you to plot points on the site plan view.
Collect stores points at the GPS Antenna #1 by time or distance.
  Both routines expect a coordinate file to be created. From the HydroStar main menu - pick OPTIONS then CONTINUE then OPTIONS then GENERAL OPTIONS then COORDINATE FILE then pick ENTER NAME and type in new filename.
Will you be using a rover with SurvStar to check points on the pile driving template prior to pile driving?
email Jim Carlson at:
jcarlson@carlsonsw.com
FOR ANY ADDITIONAL INFO...